Loma Linda Fire Prevention Bureau

25541 Barton Rd, Loma Linda CA 92354

909-799-2859

Fax 909-799-2891

Fire Watch and Impairment Requirements

Any building where a required Fire Protection system (fire alarm, sprinkler, fire pump, etc) is out of service and is occupied is required to either evacuate the building or establish an approved fire watch. The person assigned to fire watch must have at least one method of contacting the fire department in an emergency and their only duty shall be to perform constant patrols of the protected premises and keep watch for fires.  In addition the building owner is required to have an impairment coordinator. The out of service equipment must be tagged out of service and the tag placed at the fire alarm panel and the fire department connection. (Reference 2016 California Fire Code Chapter 9 Section 901.7)

Steps to take for impairment:

- 1. The extent and expected duration of the impairment have been determined.

- 2. The area or building involved has been inspected and the increased risk determined.

- 3. Recommendations have been submitted to management/building owner.

- 4. The Fire Department has been notified.

- 5. The insurance carrier, Alarm Company, building owner/ manager and other authorities having jurisdictions have been notified.

- 6. The supervisors in the area affected have been notified.

- 7. A tag impairment system has been implemented.

- 8. Necessary tools and materials have been assembled on the impairment site.

Fill in the below information and fax to the Fire Prevention Bureau

Business Name ____________________________

Address__________________________________

Impairment (check one)    __ Planned      __ Emergency

System Impaired ____________________________________________________

Date and Time out of Service __________________________

Impairment Coordinator Name___________________________ Phone #____________

Fire Watch #1________________________Fire Watch #2_____________________

Fire Watch #3________________________Fire Watch #4______________________

Tag Placement_______________________________________________________

Repair Contractor_____________________________________________________

Time returned to service_____________ Date returned to service__________________

Fire Prevention Inspector _____________________Incident#______________________

Owner/Representative________________________________________

Date____________